h = ones(100,1);
x = load('../hmwk8/marySong.mat');
x = x.marySong(1:2560);
L = 256; % size of circular buffer
P = length(h);

%% overlap add
H = fft(h,____);
y_a = zeros(______,1);
numblocks = floor(length(x)/L);
for iblock = 1:numblocks
    new_block = x(________:_______);
    New_Block = fft(new_block,_____);
    New_Out = New_Block.*H;
    new_out = ifft(New_Out,_____);
    y_a(________:_______) = y_a(_______:_____) + new_out;
end

%% overlap save
H = fft(h,__);
y_s = zeros(________,1);
x_pad = [zeros(___,1); x];
numblocks = floor((length(x_pad)-(L-P+1))/L);
for iblock = 1:numblocks
    new_block = x_pad(_______:_______);
    New_Block = fft(new_block,__);
    New_Out = New_Block.*H;
    new_out = ifft(New_Out,__);
    y_s(____________:_______) = new_out(___:___);
end